RIDOT Large-Site SWPPP TEMPLATE
Instructions

For all projects with one (1) acre or greater of disturbance, a Storm Water Pollution Prevention Plan (SWPPP) is required by the RIPDES General Permit for Stormwater Discharge Associated with Construction Activities (GP).

This document is being provided as an aid in the preparation of a SWPPP.  It is a comprehensive list of issues a SWPPP preparer must consider during the development of the document.  The items in the template are derived from the GP, the RIDEM RI Model SWPPP Template, and the Environmental Protection Agency’s model SWPPP template.

The use of this checklist does not guarantee compliance with the GP. Additionally, using the template to generate a SWPPP is not a substitute for knowledge of the permit requirements; the template serves as a guidance document only.

Instructions for SWPPP Preparers:

When converting this model SWPPP into your site-specific SWPPP, please keep in mind the following:

- Items in black should remain in the final site specific SWPPP and do not need to be modified.

- Items highlighted in gray indicate where information must be inserted. Click on the highlighted text and type response – the gray highlighting will be over-written.

- Items in blue-italics are included to provide guidance to you, the SWPPP preparer, during the development of the site specific SWPPP, these items may be deleted in the final site specific SWPPP document.

If there are any questions, please contact the

RIDOT Environmental Division at 401-734-4892.

Stormwater Pollution Prevention Plan

For:

Insert Project Name

Insert Project Site Location/Address

Insert City, State, Zip Code

| Owner: | RI DEPARTMENT OF TRANSPORTATION Alisa Diaz Richardson 2 CAPITOL HILL PROVIDENCE, RI 02903 401-222-2468 |
| --- | --- |
| Operator: TO BE DETERMINED UPON CONTRACT AWARD | Company Name Name Address City, State, Zip Code Telephone Number |
| Estimated Project Dates: | Start Date: Start Date |
|  | Completion Date: End Date |
| SWPPP Prepared By: | Company Name Preparer's Name Address City, State, Zip Code Telephone Number |
| SWPPP Preparation Date: | Date |

# OWNER CERTIFICATION

RIPDES Construction General Permit – Section V.G

I certify under penalty of law that this document and all attachments were prepared under the direction or supervision in accordance with a system designed to assure that qualified personnel properly gather and evaluate the information submitted. Based on my inquiry of the person or persons who manage the system, or those persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate, and complete.

I am aware that there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations. I am aware that it is the responsibility of the owner/operator to implement and amend the SWPPP as appropriate in accordance with the requirements of the RIPDES Construction General Permit.

________________________________________________________
Owner Signature:      	Date

Owner Name: Alisa Diaz Richardson, PE
Owner Title: Administrator, Environmental Division

Company Name:  	Rhode Island Department of Transportation

# Table of Contents

OWNER CERTIFICATION	ii

INTRODUCTION	1

ADDITIONAL RESOURCES	2

SECTION 1: SITE DESCRIPTION	3

1.1	Project/Site Information	3

1.2 	Nature and Sequence of Construction Activity	3

1.3	Existing and Proposed Soils, Slopes, Vegetation, and Drainage Patterns	3

1.4	Construction Site Estimates	4

1.5	Receiving Waters	4

1.6	Allowable Non-Storm Water Discharges	6

1.7	Existing Data of Known Discharges from Site	6

1.8	Endangered Species Certification/Natural Heritage Areas	7

1.9	Historic Preservation/Cultural Resources	7

1.10	Site Features and Sensitive Areas to be Protected	8

1.11	Potential Sources of Pollution	9

1.12	Site Plans	10

SECTION 2:  EROSION AND SEDIMENTATION CONTROLS	11

2.1	Minimize Disturbed Area and Protect Natural Features and Soil	11

2.2  	Phase Construction Activity	11

2.3	Control Stormwater Flowing Onto and Through the Project	12

2.4	Stabilizing Soils	13

2.5	Protect Slopes	14

2.6	Protect Storm Drain Inlets	14

2.7	Protect Storm Drain Outfalls	14

2.8	Establish Perimeter Controls and Sediment Barriers	15

2.9	Retain Sediment On-Site and Control Dewatering Practices	15

2.10	Monitoring Weather Conditions	15

2.11	Additional BMPs	16

2.12	Construction Site Erosion and Sediment Control BMPs	16

SECTION 3: GOOD HOUSEKEEPING BMPS	17

3.1	Off-site Tracking of Sediments	17

3.2	Waste Disposal	17

3.3	Spill Prevention and Control Plan	18

3.4	Control of Allowable Non-Storm Water Discharges	18

3.5	Establish Proper Building Material Staging Areas	19

3.6	Designate Washout Areas	19

3.7	Establish Proper Equipment/Vehicle Fueling and Maintenance Practices	20

3.8	Dust Control	20

3.9	Sweeping	21

3.10	Additional BMPs	21

3.11	Construction Site Good Housekeeping BMPs	21

SECTION 4: POST-CONSTRUCTION BMPs	22

4.1	Post-Construction BMPs	22

SECTION 5: MAINTENANCE and INSPECTIONS	23

5.1	Maintenance	23

5.2	Inspections	23

5.3	Corrective Actions	25

SECTION 6: Amendments	26

SECTION 7: Recordkeeping	27

SECTION 8: Party Certifications	28

SWPPP APPENDICES	30

Attachment A	– General Location Map	30

Attachment B	– Site Plans	30

Attachment C	– Copy of RIPDES General Permit	30

Attachment D	– Copy of RIPDES NOI	30

Attachment E	– Copy of Regulatory Permits	30

Attachment F	– Inspection Form	30

Attachment G	– Amendments Log	30

Attachment H	– Additional Information (i.e. documentation)	30

This Table of Contents is structured to be automatically populated by Microsoft Word.
Upon final completion of this template, “right-click” anywhere in the Table of Contents, select “Update Field”, and then “Update entire table”.  Page numbers will automatically be synced with the changed document.

# INTRODUCTION

This Construction Site Storm Water Pollution Prevention Plan (SWPPP) has been prepared for the State of Rhode Island Department of Transportation (RIDOT) pursuant to the Rhode Island Department of Environmental Management (RIDEM) Rhode Island Pollutant Discharge Elimination System (RIPDES) Program regulations (amended February 5, 2003).  Pursuant to Rule 32 of the RIPDES Regulations, projects proposing to discharge storm water must seek authorization under a RIPDES General Permit. In accordance with the General Permit for Storm Water Discharge Associated with Construction Activity (General Permit), projects that disturb one (1) or more acres require the preparation of a SWPPP and RIDEM authorization following RIPDES review of a Notice of Intent (NOI).   This SWPPP provides guidance for complying with the terms and conditions required under the General Permit, however, this document does not negate or eliminate the need to understand and adhere to all applicable RIPDES regulations.

The purpose of erosion and sedimentation best management practices (BMPs) is to prevent pollutants from leaving the construction site and entering waterways or environmentally sensitive areas during and after construction.  This SWPPP has been prepared prior to the initiation of construction activities to address anticipated worksite conditions.  The best management practices (BMPs) depicted on the site plan and described in this narrative should be considered the minimum measures required to control erosion, sedimentation, and stormwater runoff at the site.  Since construction is a dynamic process with changing site conditions, it is the operator’s responsibility to manage the site during the construction phases to prevent pollutants from leaving the site.  This may require the owner or operator to revise and amend the SWPPP during construction to address varying site and/or weather conditions, such as by adding or realigning erosion or sediment controls, to ensure the SWPPP remains compliant with the General Permit.  Records of these changes must be added to the amendment log attached to the SWPPP, and to the site plans as “red-lined” drawings.

The RIDOT Construction Manager and certified Inspector are required to review the SWPPP and sign the Party Certification pages (Section 8).  The prime contractor and all subcontractors involved in earthwork or exterior construction activities are also required to review the SWPPP and sign the certification pages before construction begins.

It is the responsibility of the RIDOT Construction Manager to maintain the SWPPP, including all attachments, amendments and inspection records, at the project field office and to make all records available for inspection by RIDEM during construction.  (RIPDES Construction General Permit – Section II.A.)

Any questions regarding the SWPPP, BMPs, inspection requirements, or any other facet of this document may be addressed to the RIDOT Environmental Division at 401-734-4892.

Please note:  Even if practices are correctly installed on a site according to the approved plan, the site is only in compliance when erosion and sedimentation are effectively controlled throughout the entire site.

# ADDITIONAL RESOURCES

Rhode Island Department of Transportation
Environmental Division 
360 Lincoln Avenue
Warwick, RI 02888
401-734-4892
http://www.dot.ri.gov/about/stormwater.php

Rhode Island Department of Environmental Management
Office of Water Resources 
235 Promenade Street
Providence, RI 02908
(401) 222-3961
http://www.dem.ri.gov/programs/water/ 

RIDEM RIPDES website
http://www.dem.ri.gov/programs/water/permits/ripdes/

RIDEM Water Quality website (for 303(d) and TMDL listings)
http://www.dem.ri.gov/programs/water/quality/restoration-studies/

RINHS “Natural Heritage” Species

https://rinhs.org/biodiversity-data/info-on-rare-species-in-ri/

RIDEM Geographic Data Viewer – Environmental Resource Map
http://www.dem.ri.gov/maps/index.htm

RIDEM RI Stormwater Design and Installation Standards Manual (as amended)

http://www.dem.state.ri.us/programs/benviron/water/permits/ripdes/stwater/t4guide/desman.htm

RIDEM, USDA Soil Conservation Service, and RI State Conservation Committee Soil Erosion and Sediment Control Handbook (as amended)
http://www.dem.ri.gov/programs/bnatres/water/pdf/riesc-handbook16.pdf

Rhode Island Department of Transportation Standard Specifications for Road and Bridge Design and Other Specifications and Standard Details http://www.dot.ri.gov/business/bluebook.php

Natural Resources Conservation Service - Rhode Island Soil Survey Program
http://www.ri.nrcs.usda.gov/technical/soils.html

EPA NPDES SWPPP website 
https://www.epa.gov/npdes/developing-stormwater-pollution-prevention-plan-swppp

EPA National Menu of Stormwater Best Management Practices
https://www.epa.gov/npdes/national-menu-best-management-practices-bmps-stormwater#edu

# SECTION 1: SITE DESCRIPTION

RIPDES Construction General Permit – Section IV.E.1

## 1.1	Project/Site Information

Project/Site Name:

INSERT TEXT HERE

INSERT GENERAL PROJECT OVERVIEW HERE

Project Street/Location:

INSERT TEXT HERE

INSERT GENERAL LOCATION MAP HERE

## 1.2 	Nature and Sequence of Construction Activity

RIPDES Construction General Permit – IV.E.1.b

Provide a narrative describing the nature and estimated timetable for the construction activities, including an anticipated sequence of major activities of the project, and the ultimate intended use of the project.

INSERT TEXT HERE

Estimated Project Start Date: 			INSERT DATE HERE

Estimated Project Completion Date:		INSERT DATE HERE

Estimated Number of Months: 			INSERT # HERE

## 1.3	Existing and Proposed Soils, Slopes, Vegetation, and Drainage Patterns

Provide description of pre- and post-construction site conditions

Soil type(s):

RIPDES Construction General Permit – IV.E.1.e

Provide a description of the soils at the site and of each soils' erodibility hazard as listed in the U.S. Soil Conservation Service’s Soil Survey of Rhode Island (1981).

List Location, Soil Type, Erodibility Hazard

List Additional Locations and their corresponding soil types and erodibility hazards

Slopes:

Provide a description of the slopes that will be impacted by construction activities (grading or filling)

Existing:  INSERT TEXT HERE

Proposed:  INSERT TEXT HERE

Vegetation/Impervious Area:

Provide a description of the vegetative and impervious areas that will be impacted by construction activities

Existing: INSERT TEXT HERE

Proposed: INSERT TEXT HERE

Drainage Patterns:

Provide a description of the drainage patterns that will be impacted by construction activities

Existing:  INSERT TEXT HERE

Proposed:  INSERT TEXT HERE

## 1.4	Construction Site Estimates

RIPDES Construction General Permit – IV.E.1.c & IV.E.1.d

Provide construction site estimates of the total area of the site and the total area of the site that is expected to undergo soil disturbance and the calculated pre-construction and post-construction runoff coefficients for the site.

The following are estimates of the construction site:

Total Project Area							      acres

Construction Site Area to be disturbed					      acres

Percentage impervious area before construction				      %

Runoff coefficient before construction

Percentage impervious area after construction				      %

Runoff coefficient after construction

## 1.5	Receiving Waters

Receiving waters:

RIPDES Construction General Permit – III.A.7

List the waterbody(s) that will receive stormwater from the site, including streams, rivers, lakes, coastal waters, and wetlands.  Note any stream crossings, if applicable.

List/description of receiving waters:

- INSERT TEXT HERE

Storm sewer systems:

RIPDES Construction General Permit – III.A.7

List the storm sewer system or drainage system that stormwater from the site could discharge to and the waterbody(s) that it ultimately discharges to.

Will construction site stormwater flow to any separate storm sewer systems?

( Yes		( No

If yes, list the separate storm sewer systems and if permits/permission is required:

- INSERT TEXT HERE

303(d)/TMDL waters:

RIPDES Construction General Permit – Section IV

If any of the waterbodies above are impaired (303(d) listed) and/or subject to Total Maximum Daily Loads (TMDLs), list the pollutants causing the impairment and any specific requirements in the TMDL(s) that are applicable to RIDOT.  
Visit http://www.dem.ri.gov/programs/water/quality/restoration-studies/ for more information and a list of Rhode Island impaired waters and TMDL Studies. See also the RIDEM Notice of Intent instructions

Will project site stormwater flow to any 303(d) listed or TMDL water body (include both active construction and post-construction flow)?

( Yes		( No

If yes, list & provide description of 303(d)/TMDL waters and applicable TMDL requirements:

- INSERT TEXT HERE

Special Resource Protection Waters (SRPWs):

Special Resource Protection Waters (SRPWs) are high quality surface waters identified by DEM as having significant ecological or recreational uses.  Visit Appendix D of the RIDEM Water Quality Regulations http://www.dem.ri.gov/pubs/regs/regs/water/h20q09a.pdf for more information and a list of Rhode Island SRPW waters.  See also the RIDEM Environmental Resource Map available on the DEM Maps webpage at http://www.dem.state.ri.us/maps/index.htm .

Will construction site stormwater flow to any Special Resource Protection Waters (include both active construction and post-construction flow)?

( Yes		( No

If yes, list & provide description of Special Resource Protection Waters:

- INSERT TEXT HERE

Cold Water Fisheries:

Cold Water Fisheries are freshwater rivers, streams, lakes and ponds that are designated by DEM as ‘coldwater’ based upon the potential for the presence of brook trout by evaluating current and historical presence/absence information, habitat, water quality and physical characteristics data.  Contact the DEM Office of Water Resources at 401-222-4700 for more information.  See also the RIDEM Environmental Resource Map available on the DEM Maps webpage at http://www.dem.state.ri.us/maps/index.htm.

Will construction site stormwater flow to any cold water fishery water body (include both active construction and post-construction flow)?

( Yes		( No

If yes, list & provide description of Cold Water Fisheries:

- INSERT TEXT HERE

## 1.6	Allowable Non-Storm Water Discharges

RIPDES Construction General Permit – IV.E.1.g

Discharges not comprised of Stormwater are allowed under the RIPDES Construction General Permit but are limited to the following: discharges which result from the washdown of vehicles where no detergents are used; external building washdown where no detergents are used; the use of water to control dust; fire fighting activities; fire hydrant flushings; natural springs; uncontaminated groundwater; lawn watering; potable water sources including waterline flushings; irrigation drainage; pavement washwaters where spills or leaks of toxic or hazardous materials have not occurred (unless all spilled materials have been removed) and where detergents are not used; and foundation or footing drains where flows are not contaminated with process materials such as solvents, or contaminated by contact with soils where spills or leaks of toxic or hazardous materials has occurred. If any of these discharges may reasonably be expected to be present and to be mixed with stormwater discharges, they must be specifically listed here.

Are there allowable non-storm water discharges on or near the project area?

( Yes		( No

If yes, list the sources of allowable non-Stormwater discharge (be sure to include all dewatering activity discharges).  If applicable, control measures must be documented in Section 2.12 &/or Section 3.4.

List of allowable non-stormwater discharges:

INSERT TEXT HERE

If any existing or proposed discharges consist of contaminated groundwater, such discharges are not authorized under the RIPDES Construction General Permit. These discharges must be permitted separately by seeking coverage to treat and discharge under a separate RIPDES individual permit or under the RIPDES Remediation General Permit. Contact the RIDOT Natural Resources Unit at 401-222-2023 for application requirements and additional information.

Are there any known or contaminated discharges, including dewatering operations, on or near the project area?

Yes		  No

If yes, list the discharges and the RIPDES individual permit number(s) or RIPDES Remediation General Permit Authorization number(s) associated with these discharges.

RIPDES individual permit number:  INSERT TEXT HERE

RIPDES Remediation General Permit Authorization number:  INSERT TEXT HERE

## 1.7	Existing Data of Known Discharges from Site

RIPDES Construction General Permit – IV.E.1.h

List and provide existing data (if available) on the quality of any known discharges from the site.

Are there known storm water discharges from the project area?

( Yes		( No

Describe how this determination was made:

INSERT TEXT HERE

If yes, list discharges and locations:

INSERT TEXT HERE

Is there existing data on the quality of the known storm water discharges?

( Yes		( No

If yes, provide data:

INSERT TEXT HERE

## 1.8	Endangered Species Certification/Natural Heritage Areas

RIPDES Construction General Permit – Section V

Each project authorized under the RIPDES Construction General Permit must determine if the site is within or directly discharges to a Natural Heritage Area (NHA).  DEM Natural Heritage Areas include known occurrences of state and federal rare, threatened and endangered species. Review RIDEM NHA maps to determine if there are natural heritage areas on or near the construction site. See the RIDEM Notice of Intent instructions

Are there any Natural Heritage Areas being disturbed by the construction activity or will discharges be directed to the Natural Heritage Area as a result of the construction activity?

Yes		  No

If yes, describe or refer to documentation which determines the likelihood of an impact on this area and the steps that will be taken to address any impacts.

INSERT TEXT HERE

## 1.9	Historic Preservation/Cultural Resources

Review any/all applicable federal, state, local, or Native American historic preservation laws and regulations and coordinate with the RIDOT-Cultural Resources Unit (RIDOT-CRU) to determine if there are historic properties, historic cemeteries or cultural resources on or near the construction site.

Are there any historic properties, historic cemeteries or cultural resources on or near the construction site?

( Yes		( No

Describe how this determination was made and summarize RIDOT-CRU review comments:

INSERT TEXT HERE

If yes, describe or refer to documentation which determines the likelihood of an impact on this historic property, historic cemetery or cultural resource and the steps taken to address that impact including any conditions or mitigation measures that were approved by other parties.

INSERT TEXT HERE

## 1.10	Site Features and Sensitive Areas to be Protected

The first goal in the LID site planning and design process is to avoid disturbance of natural features. This includes identification and preservation of natural areas that can be used in the protection of water resources. It is important to understand that minimizing the hydrologic alteration of a site is just as important as stormwater treatment for resource protection. Therefore, describe all site features and sensitive resources that exist at the site such as floodplains, steep slopes (>15%), erodible soils, wetlands, hydric soils, surface waters, and their riparian buffers, specimen trees, natural vegetation, forest areas, stream crossings, historic properties, historic cemeteries or cultural resources that are to be preserved.  Also include any areas that are to be designated as a Qualified Pervious Area (QPA).

Sensitive areas and measures that will be implemented to protect them:

INSERT TEXT or TABLE HERE

## 1.11	Potential Sources of Pollution

RIPDES Construction General Permit – IV.E.1.f

Provide a description of potential sources of pollution that may reasonably be expected to affect the quality of storm water discharges from the site (i.e. exposed, un-stabilized soil stockpiles, clearing and grubbing operations, vehicle tracking, concrete washouts, diesel fuel, etc.)

| Anticipated on this Project | Operation/ Location | Stormwater Pollutants |
| --- | --- | --- |
|  | Clearing, grading, excavating, and unstabilized areas | Sediment; Trash/Debris |
|  | Construction Entrance | Sediment |
|  | Soil Stockpiles | Sediment |
|  | Paving operations | Sediment; Trash/Debris |
|  | Concrete washout and waste | Heavy metals; pH; Trash/Debris |
|  | Structure construction/ painting/ cleaning | Nutrients; pH; Trash/Debris; Toxic chemicals |
|  | Demolition and debris disposal | Sediment; Trash/Debris |
|  | Dewatering operations | Sediment; Nutrients |
|  | Drilling and blasting operations | Sediment; pH; Trash/Debris |
|  | Material delivery and storage | Sediment; Nutrients; Heavy metals; pH; Pesticides/Herbicides; Oil/Grease; Trash/Debris; Toxic chemicals |
|  | Material use during building process | Nutrients; heavy metals; pH; pesticides/herbicides; oil/grease; trash/debris; toxic chemicals |
|  | Solid waste/ trash/ debris | trash/debris; toxic chemicals |
|  | Hazardous waste | heavy metals; pH; pesticides/herbicides; oil/grease; toxic chemicals |
|  | Contaminated spills | Nutrients; heavy metals; pH; pesticides/herbicides; oil/grease; toxic chemicals |
|  | Sanitary/septic waste (porta potty?) | Nutrients; pH; Bacteria/Viruses; toxic chemicals |
|  | Vehicle/equipment fueling and maintenance | Oil/Grease; Toxic chemicals |
|  | Vehicle/equipment use and storage | Oil/Grease; Toxic chemicals |
|  | Landscaping operations | Sediment; Nutrients; Trash/Debris |
|  | Off-site LUHPPL run-on | Industrial toxins; oil/grease; heavy metals; fuel; salt; hazardous materials |
|  | Other: |  |

## 1.12	Site Plans

All of the following information must be included on the Plans.  
This SWPPP may reference the complete construction plan set, and/or may have a specific SWPPP Set developed.  Please indicate the plan type (General, Drainage & Utility, SWPPP, etc..) and sheet #(s) where below information is found.  RIPDES Construction General Permit – IV.E.1.a

TITLE & DATE OF PLAN SET(S):  INSERT TEXT & DATE

| Plan/Sheet #(s) | Required Information |
| --- | --- |
|  | Total Project Area, including all grading and/or excavation, and a defined Limit of Disturbance. |
|  | Pre- and post-development drainage patterns including (but not limited to): sub-watershed limits, direction(s) of stormwater flow, locations of storm drain inlets and outfalls, existing and proposed conveyance systems (i.e. grass channels, swales, closed drainage system) |
|  | The location and name of the receiving waters &/or separate storm sewer system and the ultimate receiving waters (i.e. name of major watershed basin) |
|  | Location of resource protection areas including waters of the State, wetlands lakes, ponds, coastal shoreline features and required setbacks (e.g. buffers, water supply wells, septic systems). Indicate below whether or not the areas have been verified in the field. |
|  | Location of environmentally sensitive features/areas to be preserved &/or protected (i.e. endangered species habitats, historic sites, natural heritage areas, Qualified Pervious Areas (QPAs)) (Section 1.10) |
|  | Boundaries of existing vegetation to remain undisturbed |
|  | The location of all impervious structures (existing and proposed roads, buildings, and other structures) |
|  | Locations and timing of stabilization measures including phased clearing and grubbing based on scheduled activities |
|  | The location of all structural erosion, sediment and runoff control BMPs (i.e. sediment basins, outlet protection, etc.) |
|  | Locations of all non-structural BMPs (i.e. perimeter controls, check dams, storm drain protection, etc.) |
|  | The location of all permanent post-construction BMPs (i.e. WVTS, filtration systems, etc) |
|  | Constraint Map, indicating areas within the project limits which are unsuitable for material storage areas, equipment storage areas, designated concrete washout areas, dumpsters, stockpiles, fueling locations, etc. (i.e. locations where these activities will not occur, and recommendations of where they may occur) **(RECOMMEND SEPARATE PLAN SHEET)** Designated areas will not be within regulated wetlands, or within 50-feet of the storm drain system. |
|  | The location of spill prevention and response equipment |
| FIELD VERIFICATION INFORMATION |
| Date: Insert Date Verified by DEM: ( N/A ( No ( Yes | By: Insert Person/Company Wetland Permit Issued: ( No ( Yes # _______________ |

# SECTION 2:  EROSION AND SEDIMENTATION CONTROLS

RIPDES Construction General Permit – Section IV.E.2.a

The purpose of erosion controls is to prevent sediment from moving onto, around, or off of the construction site. Properly installed and maintained erosion controls are the primary defense against sediment pollution.

Sedimentation controls are a second line of defense against moving sediment.  The purpose is to prevent moving sediment from leaving the construction site and entering environmentally important areas.

Runoff controls are used to slow the velocity of concentrated water flows.  By intercepting and diverting stormwater runoff to a stabilized outlet or treatment BMP, erosion and sedimentation are reduced.

Please note:  Even if practices are correctly installed on a site according to the approved plan, the site is only in compliance when sediment and pollutants are effectively controlled throughout the entire site.  If controls are repeatedly failing, it is the responsibility of the Construction Manager and Construction Contractor to develop a corrective action plan that may include different controls than is depicted on the Approved Plan Set.

## 2.1	Minimize Disturbed Area and Protect Natural Features and Soil

As far as is practicable, existing vegetation will be protected and left in place, in accordance with the clearing limits shown on the approved Plans.  Prior to any land disturbance activities commencing on the site, the Contractor will physically mark limits of disturbance (LOD) on the site and any areas to be protected within the site, so that workers can see the areas to be protected.

Describe the areas that will be disturbed with each phase of construction and the BMPs (signs, fences, etc.) that will be used to protect those areas that should not be disturbed.  Describe natural features identified earlier and how each will be protected during construction activity. Also describe how topsoil will be preserved.

- INSERT TEXT

## 2.2  Phase Construction Activity

Proper sequencing of construction activities is essential to maximize the effectiveness of erosion and sediment control measures.  The purpose is to reduce the amount and duration of soil exposed to erosion by wind, rain, runoff, and vehicle tracking.

Construction sequencing and timing of construction activities will include:

- Installation of all erosion and sediment controls that are required to be in place and functional before any earthwork begins.  This will be done in accordance with Sections 201, 206 through 211 of the RIDOT Standard Specifications.

- Upon acceptable completion of site preparation and installation of erosion and sediment controls, site construction activities may commence.  Routine inspection and maintenance and/or modification of erosion and sediment controls while earthwork is being done is required.

- Final stabilization of any disturbed areas after earthwork has been completed.

Describe the intended construction sequencing and timing of major activities, including grading activities, road and utility installation, and building phases.  The first phase should include all erosion and sediment controls that are required to be in place before earthwork begins.  Phase II through XX may include erosion and sediment controls required while earthwork is being done.  The final phase should include final stabilization BMPs.

- Phase I – BEFORE EARTHWORK

Describe phase

Duration of phase (start date, end date)

List BMPs associated with this phase

Describe stabilization methods for this phase (describe any temporary stabilization methods that will be used before final stabilization)

- Phase II – DURING EARTHWORK

Describe phase

Duration of phase (start date, end date)

List BMPs associated with this phase

Describe stabilization methods for this phase (describe any temporary stabilization methods that will be used before final stabilization)

Add additional phases as required

- Phase III – FINAL STABILIZATION

Describe phase

Duration of phase (start date, end date)

List BMPs associated with this phase

Describe stabilization methods for this phase (describe any temporary stabilization methods that will be used before final stabilization)

## 2.3	Control Stormwater Flowing Onto and Through the Project

Structural BMPs will be used to prevent stormwater flow from coming onto the project area, and to divert and slow on-site stormwater flow from exposed soils to limit erosion, runoff, and the discharge of pollutants from the site.

Control measures &/or methods that may be used include diversion ditches or berms, compost filter socks, fiber rolls, gravel bag berms, slope drains, check dams, and riprap.

Describe controls, including design specifications and details, to be used to divert flows from exposed soils, retain or detain flows, or otherwise limit runoff and the discharge of pollutants from exposed areas of the site.

- INSERT TEXT

## 2.4	Stabilizing Soils

Phased Clearing & Grubbing:

Only areas that can be reasonably expected to have active construction work being performed within
21-days of disturbance will be cleared/grubbed at any one time.  It is NOT acceptable to clear and grub the entire construction site if disturbed portions will not be active within the 21-day time-frame.

Clearing/Grubbing will not take place during a rain event if erosion is likely to occur; nor will it occur if a rain event is forecasted and appropriate erosion controls can not be installed prior to the storm and in accordance with section 201, 206 through 211 of the RIDOT standard specifications.

No undisturbed areas will be cleared of existing vegetation after October 15th of any calendar year or during any period of full or limited winter shutdown. All disturbed soils exposed prior to October 15 of any calendar year will be seeded or protected by that date.  Any such areas that do not have adequate vegetative stabilization, as determined by the Construction Manager or environmental inspector, by November 15 of any calendar year, must be stabilized through the use of erosion control matting or hay mulch, in accordance with specifications contained within the RI Soil Erosion and Sediment Control Handbook (as amended).  If work continues within any of these areas during the period from October 15 through April 15, care must be taken to ensure that only the area required for that Day’s work is exposed, and all erodible soil must be restabilized within 5 working days.

As per RIDOT Standard Specification 201.03.1 – Clearing and Grubbing: 
After clearing, and by the end of each day's grubbing operation, the Contractor will install erosion control measures that are indicated on the Plans or as directed by the Construction Manager. Such erosion control measures will be installed in strict accordance with the requirements of SECTIONS 206, 207, and 208 of these Specifications, PERIMETER EROSION CONTROLS, CHECK DAMS, and TEMPORARY DEWATERING BASINS, respectively.

Initiating Stabilization Practices

As per RIPDES General Permit (Construction Activity) Section IV.E.2.a:
Upon completion and acceptance of site preparation and initial installation of erosion and sediment controls the operator will initiate appropriate stabilization practices during all phases of construction on all disturbed areas as soon as possible but not more than fourteen (14) days after the construction activity in that area has temporarily or permanently ceased, unless the activity is to resume within twenty one (21) days.

Any disturbed areas that will not have active construction activity occurring within twenty one (21) days must be stabilized using the BMPs depicted on the approved plan set and in accordance with RIDOT Standard Specifications Section L.02 – Seeding, Section L.05 - Seed Stabilizers and Section M.18 – Landscape Materials (M.18.08 – Mulch and M.18.09 – Seed Stabilizer Materials).

Maintaining Stabilization

Controls and methods that may be used to maintain soil stabilization include the placement of geotextiles, erosion control blankets/mats, and temporary seeding.  If the stabilization BMPs fail and erosion occurs, then alternative control measures &/or methods may need to be substituted, with approval of the RIDOT Construction Manager and the RIDOT Environmental Division.

Describe controls, including design specifications and details, to be used to stabilize soils throughout the entire duration of the Construction project.

INSERT TEXT

## 2.5	Protect Slopes

Controls will be used to protect slopes from erosion from concentrated stormwater flow.

Slopes that will have concentrated stormwater flow will be protected using the BMPs depicted on the approved plan set and in accordance with RIDOT Standard Specifications Sections 202, 206 – 211, or any method approved of by the RIDOT Construction Manager and the RIDOT Office of Stormwater Management.

Control measures &/or methods that may be used to protect slopes include pipe slope drains, compost filter socks, fiber rolls, gravel bag berms, erosion control mats/blankets, and temporary vegetative cover.

Describe controls, including design specifications and details, to be used to protect slopes.

- INSERT TEXT

## 2.6	Protect Storm Drain Inlets

Storm drain inlet protection measures will be used to prevent soil and debris from entering storm drain inlets. These measures are usually temporary and are implemented before a site is disturbed.  ALL stormwater inlets &/or catchbasins that are operational during construction and may receive sediment-laden stormwater flow from the construction site must be protected using any of the BMPs outlined in the RIDOT Standard Specifications Section 209 – Storm Drain Protection, or any method approved of by the RIDOT Construction Manager and the RIDOT Environmental Division.

Control measures &/or methods that may be used include compost filter socks, fiber rolls, gravel bag berms, or catch basin inserts.

Describe controls, including design specifications and details, to be used to protect all inlets receiving stormwater from the project during the entire duration of the project.

- INSERT TEXT

## 2.7	Protect Storm Drain Outfalls

Outfall protection will be used to prevent scour or severe erosion at discharge points. Outfalls often have high velocity, high volume flows, and require strong materials that will withstand the forces of the water. The function of these BMPs is to protect the soil surface, reduce velocity, and promote infiltration.  Storm drain outlet BMPs also offer a last line of protection against sediment entering environmentally sensitive areas.

All stormwater outfalls that may discharge sediment-laden stormwater flow from the construction site must be protected.

Control measures &/or methods that may be used include compost filter socks, fiber rolls, gravel bag berms, or silt fence.

Describe controls, including design specifications and details, to be used to protect outlets discharging stormwater from the project during the entire duration of the project.

- INSERT TEXT

## 2.8	Establish Perimeter Controls and Sediment Barriers

Perimeter controls will be used to prevent soil erosion and stop sediment from leaving the site.  Perimeter controls will be installed, and maintained, as depicted on the approved plan set and in accordance with RIDOT Standard Specifications Section 201, 206 – 211, Perimeter Erosion Controls (installation) and Section 212 – Maintenance and Cleaning of Erosion and Pollution Controls (maintenance).

Control measures &/or methods that may be used include compost filter socks, fiber rolls, gravel bag berms, or silt fence.

Describe controls, including design specifications and details, to be used to filter and trap sediment before it leaves the construction site.

- INSERT TEXT

## 2.9	Retain Sediment On-Site and Control Dewatering Practices

Sediment traps, basins, and barriers are used to retain sediment on the site to protect streams, lakes, drainage systems, and adjacent property. These devices are used at the outlets of channels, diversions, and other runoff conveyance measures to allow sediment-filled water to pool and sediment to settle. These measures are often used as the last line of defense to stop sediment from leaving the site.

The dewatering of non-contaminated non-stormwater (i.e. groundwater) or accumulated precipitation discharge of sediment-laden water into storm drains, streams, lakes or wetlands prior to sediment removal is prohibited.

The dewatering of contaminated non-stormwater cannot be discharged without prior notice and approval from either (RIDEM) or the Coastal Resources Management Council (CRMC).  Should dewatering of contaminated water be occurring on this construction project, appropriate permits will have been obtained, and will be included as part of the Contract Documents.

Describe controls, including design specifications and details, to be used to retain sediments on-site.  Describe dewatering practices that will be implemented if water must be removed from an area so that construction activity can continue.

- INSERT TEXT

## 2.10 Monitoring Weather Conditions

Care will be taken to avoid having unstabilized areas exposed during precipitation events.  Weather forecasts will be routinely checked, and in the case of an expected precipitation event of over 0.25-inches over a 24-hour period, all BMPs will be inspected, and maintained as necessary, prior to the weather event.

In the case of an extreme weather forecast (greater than one-inch of rain over a 24-hour period), additional erosion/sediment controls will be installed where appropriate.

List the weather gauge station that will be utilized to monitor weather conditions on the construction site.   See www.wunderground.com or www.weather.gov for available stations.

- INSERT TEXT

## 2.11 Additional BMPs

Describe additional BMPs that may not fit into the above categories.

- INSERT TEXT

## 2.12 Construction Site Erosion and Sediment Control BMPs

Complete the following table for each location where Erosion and Sediment Control BMPs will be utilized.  This table is to be used as part of the SWPPP Inspection Report – please fill out accordingly.

It is expected that this table will be amended as needed throughout the construction project.

| Location/Station | BMP Description/ Standard Spec Ref | Maintenance Requirement | Phase |
| --- | --- | --- | --- |
| Perimeter | Compost Filter Sock/Silt Fence. 206.01.3/9.3.0 | 212.03.1 Sediment accumulated half way up sock; break through or significant strain of barrier | Phase I, II, III, IV |
| 82 + 80, 36’ LT | Sandbag Gutter Inlet Sediment Barrier 209.01.1 | 212.03.1 Sediment accumulated half way up barrier; break through or significant strain of barrier | Phase I, II, III |
| INSERT TEXT |  |  |  |

# SECTION 3: GOOD HOUSEKEEPING BMPS

RIPDES Construction General Permit – Section IV.E.2.c

The purpose of good housekeeping is to prevent daily construction activities from causing pollution.

Describe the key good housekeeping and pollution prevention measures that will be implemented to control pollutants in stormwater.  Examples BMPs include the proper management of waste, material handling and storage, and equipment/vehicle fueling/washing/maintenance operations.

Include RIDOT Standard Specification or Standard Detail reference with maintenance requirements.

## 3.1	Off-site Tracking of Sediments

RIPDES Construction General Permit – IV.E.2.c.i

Any construction site access point will employ the BMPs depicted on the approved plan set and in accordance with RIDOT Standard Specifications Section 211 – Construction Accesses, or any method approved of by the RIDOT Construction Manager and the RIDOT Environmental Division.   Construction accesses will be used in conjunction with the stabilization of construction roads to reduce the amount of mud picked up by construction vehicles. All RI STD 9.9.0 Construction Access roads will be constructed prior to any roadway accepting construction traffic.

If a Construction Access BMP is not designated on the plans, it is still the responsibility of the Operator to ensure that no sediment is tracked off of the construction site by any vehicles leaving the site.  Additional control measures that may be used, upon approval, include a vehicle washing station and daily street sweeping.

The Operator will remain responsible for the clean-up of any mud or dirt that is tracked onto streets or paved areas, even with the installation of gravel construction entrances.   Inspect access for excessive sediment build up. Remove sediment and rebuild the exit as necessary to retain effectiveness and prevent off-site tracking. Additional street cleaning may be required if unable to retain sediment on site.

Describe location(s) of vehicle entrance(s) and exit(s), procedures to remove accumulated sediment off-site (i.e., vehicle tracking), and stabilization practices (i.e., stone pads and/or wash racks) to minimize off-site vehicle tracking of sediments and discharges to stormwater.

- INSERT TEXT

## 3.2	Waste Disposal

RIPDES Construction General Permit – IV.E.2.c.ii

Building materials and other construction site wastes will be properly managed and disposed of to prevent the discharge of solid materials from wind and precipitation.  All types of waste generated at the site will be disposed of in a manner consistent with State Law and/or regulations.

- The waste collection area will not be within any of the constraint areas located on the “Constraint Map” (Section 1.12) and will be approved by the RIDOT Construction Manager.

- All waste containers will be covered to avoid contact with wind and precipitation.

- Waste collection will be scheduled frequently enough to prevent containers from overfilling.

- All construction site wastes will be collected, removed, and disposed of in accordance with applicable regulatory requirements and only at authorized disposal sites.

- Equipment and containers will be checked for leaks, corrosion, support or foundation failure, or other signs of deterioration.  Those that are found to be defective will be immediately repaired or replaced.

Describe measures (i.e., trash disposal, sanitary wastes, recycling, and proper material handling) to prevent the discharge of solid materials. All types of waste generated at the site must be disposed of in a manner consistent with State Law and/or regulations.

- INSERT TEXT

## 3.3	Spill Prevention and Control Plan

RIPDES Construction General Permit – IV.E.2.c.iii

Spills and leaks will be avoided through frequent inspection of equipment and material storage areas.   Heavy equipment and other vehicles will be routinely inspected for leaks and repaired as necessary. Material storage areas will be routinely inspected for leaky containers, open containers, or improper storage techniques that may lead to spills or leaks.  Appropriate cleanup procedures and supplies will be available on-site.

Spills will be cleaned up immediately and following proper response procedures and in accordance with any applicable regulatory requirements.  At no time will spills be cleaned and flushed down storm drains or in to any environmentally sensitive area (i.e. stream, pond, wetland).

Equipment/vehicle fueling and repair/maintenance operations or hazardous material storage will not take place within any of the constraint areas located on the “Constraint Map” (Section 1.12) and will be approved by the RIDOT Construction Manager.

Describe all areas where potential spills can occur, and their accompanying drainage points, and describe the spill prevention and control plan to reduce the chance of spills, stop the source of spills, contain and clean up spills, dispose of materials contaminated by spills, and train personnel responsible for spill prevention and control.

INSERT TEXT

## 3.4	Control of Allowable Non-Storm Water Discharges

RIPDES Construction General Permit – IV.E.2.c.iv

Non-storm water discharges must also be controlled to reduce the likelihood of contamination of the ‘clean’ water.  Allowable discharges should be kept separate from stormwater flow through the use of BMPs.

For contaminated non-stormwater discharge(s), the requirements and regulations of the associated  RIPDES individual permit or RIPDES Remediation General Permit must be adhered to at all times.

For the allowable non-stormwater discharge(s) associated with construction activity identified in Section 1.6, describe controls and measures that will be implemented at those sites to minimize pollutant contamination.

INSERT TEXT

## 3.5	Establish Proper Building Material Staging Areas

RIPDES Construction General Permit – IV.E.2.c.v

Stock pile management consists of procedures and practices designed to minimize or eliminate the discharge of stockpiled material (soil, topsoil, base material, rubble) from entering drainage systems or water courses.

Stock piles will not be located within any of the constraint areas located on the “Constraint Map” (Section 1.12) and will be approved by the RIDOT Construction Manager.  They will have side slopes no greater than 30% and stockpiles of erodible material will be seeded and ringed with RI STD 9.1.0 to stabilize (or RIDOT approved equivalent: berms, dikes, fiber rolls, compost socks, sandbag, gravel bags).

If soil stockpiles are not stabilized with vegetation, then they must be securely covered at the end of each workday.

All chemicals and/or hazardous waste material must be stored properly and legally in covered areas, with containment systems constructed in or around the storage areas. Areas must be designated for materials delivery and storage. Designated areas will not be located within any of the constraint areas located on the “Constraint Map” (Section 1.12) and will be approved by the RIDOT Construction Manager.

Describe construction materials expected to be stored on-site and procedures for storage of materials to minimize exposure of the materials to stormwater.

INSERT TEXT

## 3.6	Designate Washout Areas

RIPDES Construction General Permit – IV.E.2.c.v

Concrete mixer trucks and chutes will be washed in a designated area or concrete wastes will be properly disposed of off-site.  Washout areas for concrete, paint or any other material will not be within any of the constraint areas located on the “Constraint Map” (Section 1.12) and will be approved by the RIDOT Construction Manager.

Temporary concrete washout areas must be constructed and maintained to contain all water and concrete waste generated by washout operations. A sign should be placed at the washout site to inform concrete equipment operators of the facility location.  Facilities must be cleaned or replaced when they reach 75% capacity.

At no time will any material (concrete, paint, chemicals) be washed into storm drains, open ditches, streets, streams, wetlands, or any environmentally sensitive area.  The site operator must ensure that construction waste is properly and legally disposed of, to avoid exposure to precipitation, at the end of each working day. Designated areas will not be located within any of the constraint areas located on the “Constraint Map” (Section 1.12) and will be approved by the RIDOT Construction Manager.

Describe location(s) and controls to minimize the potential for stormwater pollution from washout areas for concrete mixers, paint, stucco, etc.

INSERT TEXT

## 3.7	Establish Proper Equipment/Vehicle Fueling and Maintenance Practices

RIPDES Construction General Permit – IV.E.2.c.v

Vehicle fueling, maintenance and/or washing will occur off-site, or in designated areas.  Designated areas will not be located within any of the constraint areas located on the “Constraint Map” (Section 1.12) and will be approved by the RIDOT Construction Manager.

Areas will be clearly designated, and berms, sandbags, or other barriers will be used around the perimeter of the maintenance area to prevent storm water contamination.

Construction vehicles will be inspected frequently for leaks.  Repairs will take place immediately. Disposal of all used oil, antifreeze, solvents and other automotive-related chemicals will be according to applicable regulations; at no time will any material be washed down the storm drain or in to any environmentally sensitive area.

Describe equipment/vehicle fueling and maintenance practices that will be implemented to control pollutants to stormwater (e.g., secondary containment, drip pans, spill kits, etc.)

INSERT TEXT

## 3.8	Dust Control

RIPDES Construction General Permit – IV.E.2.c.v

Dust control procedures and practices will be used to suppress dust on a construction site during the construction process, as applicable.   Precipitation, temperature, humidity, wind velocity and direction will determine amount and frequency of applications. However, the best method of controlling dust is to prevent dust production. This can best be accomplished by limiting the amount of bare soil exposed at one time.  RIDOT Standard Specifications Section 907 – Dust Control – will be followed.

Dust Control methods may include watering, surface roughening, wind barriers, walls, and covers.

Describe dust control practices that will be implemented to control pollutants to stormwater.

INSERT TEXT

## 3.9	Sweeping

RIPDES Construction General Permit – IV.E.2.c.v

Sweeping of streets, roads, highways and parking lots that have accumulated significant amounts of pollutants (construction site sediment, trash, debris) will be done as necessary, or as directed by the RIDOT Construction Manager.   When construction exits are not keeping construction site sediment from the roadway, sweeping will be done on a daily basis.  Disposal of collected sweeping material will follow RIDOT Standard Specifications Section 931 – Cleaning and Sweeping Pavement.

Describe sweeping practices and schedule that will be implemented to control pollutants to stormwater.

INSERT TEXT

## 3.10 Additional BMPs

Describe any additional BMPs that don’t fit into the above categories.  Indicate the problem they are intended to address.

INSERT TEXT

## 3.11 Construction Site Good Housekeeping BMPs

Complete the following table for each location where Good Housekeeping BMPs will be utilized.  This table is to be used as part of the SWPPP Inspection Report – please fill out accordingly.

It is expected that this table will be amended as needed throughout the construction project.

Example:

| Location/Station | BMP Description/ Standard Spec Ref | Maintenance Requirement | Phase |
| --- | --- | --- | --- |
| Construction Site Entrance/Exit | Rock/RipRap entrance pad 211.03/9.9.0 | Replenish/Replace aggregate if it becomes clogged with sediment and is no longer effectively preventing sediment from being tracked into street | Phase I, II, III, IV |
| Adjacent Roads | Public roads adjacent to a construction site will be cleaned at the end of each day 211.01.1 | Street Sweep if construction site sediment is visible | Phase I, II, III, IV |
| Site Wide | Pick up of construction trash and debris | All loose trash and debris must be disposed of properly at the end of each working day | Phase I, II, III, IV |
| INSERT TEXT |  |  |  |

# SECTION 4: POST-CONSTRUCTION BMPs

RIPDES Construction General Permit – Section IV.E.2.b

Post-Construction Best Management Practices are BMPs that are installed during the Construction Phase of a project to manage storm water flow after the construction project is completed.

Measures must be installed during the construction project to protect permanent or long term BMPs as they are installed so that they will function properly when they are brought online at the end of the construction phase.

Such long-term BMPs may include: infiltration basins, open vegetated swales and natural depressions, vegetated buffer strips, and detention/ retention structures.  Controls may also be needed to prevent or minimize erosion at outfall locations or along the length of vegetated channels to reduce velocity flow from the structure to the receiving waters.

Control measures that may need to be implemented during the construction phase typically include measures to ensure proper installation of the long-term BMPs.  Examples include:  ensuring proper material staging areas, equipment routing (i.e. do not allow construction equipment to compact areas where infiltration BMPs will be installed), and final cleaning of structural BMPs before construction finalization.

## 4.1	Post-Construction BMPs

Describe all post-construction stormwater management measures that will be installed during the construction process to control pollutants in stormwater discharges after construction operations have been completed.

For each BMP, identify measures that are required to protect the BMP during the construction phase of the project to ensure that they will function appropriately once they are brought online.

INSERT TEXT OR TABLE HERE

Example

| Location/Station | BMP Description/ Standard Spec Ref | Protective Measures | Phase |
| --- | --- | --- | --- |
| 77 + 13, 32’ RT | Stormwater Swirl Chamber (manuf. details on plans) | Clean/Flush prior to bringing online | IV |
| 99+ 30 | Infiltration Basin RI Stormwater Design & Installation Standards Manual | Do not allow construction vehicles to compact soils where Basin is to be installed; Do not stockpile materials on Basin site | II |
| INSERT TEXT |  |  |  |

# SECTION 5: MAINTENANCE and INSPECTIONS

RIPDES Construction General Permit – Section IV.E.2.d

## 5.1	Maintenance

Maintenance procedures for erosion and sedimentation controls and stormwater management structures/facilities are described on the plans, in Section 212 of the RHODE ISLAND DEPARTMENT OF TRANSPORTATION Standard Specifications for Road and Bridge Construction August 2023 EDITION (as amended), and in the Stormwater Management Analysis documentation.

As cited:

212.03 CONSTRUCTION METHODS. Erosion and pollution controls will be maintained by the Contractor to the satisfaction of the Construction Manager. Erosion and pollution controls must be able to prevent, under normal weather conditions, both the movement of soil materials and the intrusion of sediment-laden discharges into environmentally sensitive areas.

Construction will not commence or continue until all specified erosion and pollution controls are in place, properly installed and accepted by the Construction Manager.

Erosion and pollution controls will be routinely inspected by the SWPPP Inspector. The SWPPP Inspector or Construction Manager will notify the Contractor immediately if problems develop. The Contractor will commence cleaning and maintenance measures no later than the next consecutive calendar day after receiving a directive from the Construction Manager to perform such measures. The Contractor will aggressively and expeditiously perform such cleaning and maintenance work until the original problem is remedied to the complete satisfaction of the Construction Manager. In the event of a weekend storm, the Contractor must have resources available to restore, and, if necessary, to replace any damaged controls.

The Contractor is required to have a full-time, on-site designated contact person responsible for working with the RIDOT Construction Manager and the SWPPP Inspector to resolve SWPPP-related issues.

## 5.2	Inspections

RIPDES Construction General Permit – Section II.B & Section II.D

Minimum Monitoring and Reporting Requirements

All storm water control measures, disturbed areas, areas used for the storage of materials that are exposed to precipitation (including unstabilized soil stockpiles), discharge locations, and locations where vehicles enter or exit the site must be inspected at least once every seven (7) calendar days and within twenty-four (24) hours after any storm event which generates at least 0.25-inches of precipitation per twenty four (24) hour period and/or after a significant amount of runoff or snowmelt.  An appropriate rain gauge (as identified in Section 2.4 of this SWPPP)) will be utilized for the determination of the storm events.

It is the responsibility of the RIDOT Construction Manager to coordinate with the designated SWPPP Inspector listed in SECTION 8 of this document to initiate site inspections.   Inspections will begin as soon as the Contractor is mobilized and on site.

General Notes

- The SWPPP Inspector will prepare a separate inspection report for each inspection.

- The Inspection Reference Number will be a combination of the 
Construction Contract Number - consecutively numbered inspections.
ex/ Inspection reference number for the 4th inspection of a project would be:
 		2011-AA-BBB-4

- Each report will be signed and dated by the SWPPP Inspector and forwarded to the Construction Manager within 24 hours of the inspection.

- Each report will be signed and dated by the Construction Manager and forwarded to the Contractor’s designated representative.

- Each report will be signed and dated by the Contractor upon receipt.

- If Corrective Actions are required, the Contractor will initiate appropriate measures within 24 hours of receiving of the inspection report.

- It is the responsibility of the RIDOT Construction Manager to maintain a copy of the SWPPP, copies of all completed inspection reports, and amendments as part of the SWPPP documentation at the project field office during construction.

Submitting Reports to the ED

- On a monthly basis, the inspector must electronically submit a PDF of the Inspection Reports to the Environmental Division (ED).  Please submit SWPPP Inspection Reports to: dot.swppp@dot.ri.gov .

Monthly submission:

  - must include each completed, dated, and signed inspection report, including any associated photos.

  - must be submitted no later than the 10th of the month following the end of the reporting period.

  - must include a copy of the daily rainfall summary data for the month as reported by the selected rain gauge (ex/ the monthly calendar from www.wunderground.com).

  - may have the report content, frequency, &/or submission format changed with approval from the ED.

A copy of the inspection report is attached.

REFERENCE ATTACHMENT

## 5.3	Corrective Actions

RIPDES Construction General Permit – Section II.C

If, in the opinion of the Construction Manager, corrective action is required, the Construction Manager will note it on the inspection report and will notify and direct the Contractor to take corrective action and make all necessary repairs whenever maintenance of the erosion and pollution controls is required.

In accordance with the SWPPP and Section 212 of the RIDOT Standard Specifications, the Contractor will commence with the requisite cleaning and maintenance measures no later than the next consecutive calendar day after receiving such a directive from the Construction Manager, and will aggressively and expeditiously perform such cleaning and maintenance work until the original problem is remedied to the complete satisfaction of the Construction Manager.

In accordance with the General Permit and the SWPPP, non-compliance issues will be addressed no later than seven (7) calendar days from the date of inspection.

If the Construction Manager decides on any given day that those erosion and pollution controls specified in the Contract are not in place or have not been adequately maintained as specified in this Section, the daily charge set forth in Section 212 will be deducted from monies due the Contractor as a charge for failure to comply with this Specification. Moreover, the stated daily charge will continue each consecutive calendar day thereafter until the deficiencies noted have been corrected to the complete satisfaction of the Construction Manager.

# SECTION 6: Amendments

RIPDES Construction General Permit – Section IV.D

This SWPPP is intended to be a working document.  It is expected that amendments will be required throughout the construction of the project.  Even if practices are installed on a site according to the approved plan, the site is only in compliance when erosion and sedimentation are effectively controlled throughout the entire site.

The SWPPP will be amended whenever there is a change in design, construction, operation, maintenance or other procedure which has a significant effect on the potential for the discharge of pollutants, or if the SWPPP proves to be ineffective in achieving its objectives (i.e. the selected BMPs are not effective in controlling erosion or sedimentation).

All revisions must be recorded in the Record of Amendments Log Sheet within the SWPPP, and dated red-line drawings and/or a detailed written description must be appended to the SWPPP.  Inspection Forms must be revised to reflect all amendments. Update the Revision Date and the Version # in the footer of the Report to reflect amendments made.

All SWPPP Amendments, except minor non-technical revisions, must be approved by the Construction Manager.

Attach a copy of the Amendment log

REFERENCE ATTACHMENT

# SECTION 7: Recordkeeping

RIPDES Construction General Permit – Section II.A & Section II.D

It is the RIDOT Construction Manager’s responsibility to have the following documents at the Field Office and immediately available for RIDEM review upon request:

A copy of the fully signed and dated SWPPP, which includes:

  - The signed and certified NOI form or permit application form 
INCLUDED AS ATTACHMENT ______

  - A copy of the RIPDES General Permit 
INCLUDED AS ATTACHMENT ______

  - A copy of any regulatory permits (RIDEM Freshwater Wetlands Permit, CRMC, RIDEM Water Quality, etc)  
INCLUDED AS ATTACHMENT ______

  - SWPPP Amendment Log
INCLUDED AS ATTACHMENT ______

Copies of all signed and dated Inspection reports

# SECTION 8: Party Certifications

RIPDES Construction General Permit – Section V.G

All parties working for the Rhode Island Department of Transportation are required to comply with the Stormwater Pollution Prevention Plan (SWPPP) for any work that is performed on-site.  Any person or group who violates any condition of the SWPPP may be subject to substantial penalties or loss of contract.  Contractors and Sub-Contractors are encouraged to advise all employees working on this project of the requirements of the SWPPP.  A copy of the SWPPP is available for your review at the RIDOT Field Office, or may be found in your contract documents.

The prime contractor and each subcontractor engaged in activities at the construction site that could impact stormwater must be identified and sign the following certification statement.

I acknowledge that I have read and understand the terms and conditions of the SWPPP for the above designated project and agree to follow the BMPs and practices described in the SWPPP.

RIDOT Construction Manager:

Insert Name & Title

Insert Address	____________________________

Insert City, State, Zip Code	signature/date

Insert Telephone Number, Insert Email

Certified SWPPP Inspector:

Insert Company or Organization Name

Insert Name & Title

Insert Address	____________________________

Insert City, State, Zip Code	signature/date & cert. with cert. #

Insert Telephone Number, Insert Email

Contractor SWPPP Contact:

Insert Company or Organization Name

Insert Name & Title

Insert Address	____________________________

Insert City, State, Zip Code	signature/date

Insert Telephone Number, Insert Email

SubContractor SWPPP Contact:

Insert Company or Organization Name

Insert Name & Title

Insert Address	____________________________

Insert City, State, Zip Code	signature/date

Insert Telephone Number, Insert Email

Insert more contact/signature lines as necessary

# SWPPP APPENDICES

Attach the following documentation to the SWPPP:

## Attachment A	– General Location Map

## Attachment B	– Site Plans

## Attachment C	– Copy of RIPDES General Permit may be found at https://www.dot.ri.gov/business/documents/Environmental_Division/2020%20RIPDES%20Construction%20General%20Permit%C2%A0.pdf

## Attachment D	– Copy of RIPDES NOI

## Attachment E	– Copy of Regulatory Permits

## Attachment F	– Inspection Form

## Attachment G	– Amendments Log

## Attachment H	– Additional Information (i.e. documentation)

Large-Site SWPPP Inspection Report
Instructions

For all projects with one (1) acre or greater of soil disturbance, RIDOT is required to develop and enforce a Site-Specific Stormwater Pollution Prevention Plan (SWPPP) in order to remain in compliance with the Rhode Island Pollutant Discharge Elimination System General Permit for Stormwater Discharges Associated with Construction Activities (RIPDES Construction General Permit).  As part of the SWPPP, a site-specific inspection report must be created and utilized.

ALL RIDOT staff, Contractors, and Sub-Contractors who are responsible for Erosion and Sediment Control on RIDOT construction sites are required to understand the RIPDES Construction General Permit requirements and the SWPPP.

Preparing the Inspection Report

This inspection report template has been provided by RIDOT for the development of the site-specific SWPPP Inspection Report.  It must be customized for each individual Project to meet the requirements of the RIPDES Construction General Permit (CGP).

It is expected that this Inspection Report will be prepared as part of the preparation of the site-specific SWPPP.  This inspection report template is designed to be customized according to the SWPPP document (initially) and then customized based on conditions at the site.

Review the site-specific SWPPP and the Plans to develop the inspection report.  On a copy of the site plan, number all stormwater BMPs and areas of the site that will be inspected.  Include both structural (basins, outlet protection, swales, etc) and non-structural (construction entrances, perimeter barriers, trash areas, etc) BMPs and areas that will be inspected.  Also, identify all point source outfalls, areas of highly erodible soils, and the priority natural resource areas (i.e. streams, wetlands, mature trees, etc).  List each BMP or area to be inspected separately in the site-specific BMP section of the inspection report.

An appropriate rain gauge must be identified and utilized for the determination of the storm events.  Rain gauges may be found on www.wunderground.com, www.nws.noaa.gov (or similar sites).

SWPPP Inspection Report Instructions for:

RIDOT ENVIRONMENTAL DIVISION

- The RIDOT Administrator of the Environmental Division must review the SWPPP and sign the Certification Statement as the site OWNER on p. ii of the SWPPP.

Construction Manager

- The RIDOT Construction Manager (CM) must review the SWPPP and sign the Certification Statement for RIDOT Construction Manager in Section 8.  If the RE has any questions, contact the RIDOT Environmental Division (ED) at 401-734-4892.

- It is the responsibility of the RIDOT Construction Manager to ensure that the SWPPP Inspections start BEFORE EARTHWORK BEGINS.  Earthwork is NOT allowed to proceed until a SWPPP Inspection of the site has been completed.

- After an inspection has been performed, the CM must sign the ‘acknowledgement’ certification on Page 1 of the Inspection Report at time of receipt from the Inspector.

- The CM must review the Inspection Report within 24-hours of receipt.

  - If the CM agrees with the Inspection report, the CM must:

    - Fill out the “NOTICE TO CONTACTOR” box on the last page of the Report

    - Have the Contractor sign the ‘acknowledgement’ certification on Page 1 of Report

    - Make a copy of the Inspection Report with all 3 signatures for the Contractor’s use 
AND provide a copy to the Inspector

  - If the CM disagrees with a corrective action item, the CM must:

    - Document objection with each item and provide justifiable reason in the inspection report.  The contractor will not responsible for initiating corrective actions for such items.  RIDOT’s ED will review such items if warranted.

    - Fill out the “NOTICE TO CONTACTOR” box on the last page of the Report

    - Have the Contractor sign the ‘acknowledgement’ certification on Page 1

    - Make a copy of the Inspection Report with all 3 signatures for the Contractor’s use 
AND provide a copy to the Inspector

- It is the responsibility of the RIDOT Construction Manager to maintain a copy of the SWPPP, copies of all completed & signed inspection reports, amendments, and Corrective Action Log as part of the SWPPP documentation at the project field office during construction.

- The Inspection Report serves as the RIDOT directive to the Contractor to proceed with corrective actions.

- Progress on Corrective Action items will be documented by the CM in subsequent inspections.

- On a monthly basis, the CM must electronically submit a PDF of the Inspection Reports to the Environmental Division (ED).  Please submit reports to: dot.swppp@dot.ri.gov .

Monthly submission:

  - must include each completed, dated, and signed inspection report, including any associated photos.

  - must be submitted no later than the 10th of the month following the end of the reporting period.

  - must include a copy of the daily rainfall summary data for the month as reported by the selected rain gauge (ex/ the monthly calendar from www.wunderground.com).

  - may have the report content, frequency, &/or submission format changed with approval from the ED.

CERTIFIED SWPPP INSPECTORS

- The Contractor-designated certified inspector must sign the Certification Statement for Certified SWPPP Inspector in Section 8 of the SWPPP.

- A separate inspection report will be prepared for each inspection.

- Complete any items that will remain constant, such as the project information and BMP locations and descriptions.  Then print out multiple copies (double-sided!) of this customized inspection report to use during the inspections or save the file for future use on a computer.

- The Inspection Reference Number shall be a combination of the 
Construction Contract Number - consecutively numbered inspections.
ex. Inspection reference number for the 4th inspection of a project would be:
 		2006-AA-BBB-4

- Check the rain gauge for past & future weather data prior to inspection.

- Minimum Monitoring and Reporting Requirements

“…the site must be inspected at least once every seven (7) calendar days and within twenty-four (24) hours after any storm event which generates at least 0.25-inches of precipitation per twenty-four (24) hour period and/or after a significant amount of runoff or snowmelt.” (per RIPDES CGP)

- When conducting the inspection, walk the site by following the site map and numbered BMPs locations for inspection. Also, note whether the overall site issues have been addressed.

- Take photos to document issues, completed required maintenance/corrective actions – each photo should be dated and have a unique identification # and written description indicating where it is located within the project area.  If a close-up photo is required, it should be preceded with a photo including both the detail area and some type of visible fixed reference point.  Photos should be annotated with Station numbers and other identifying information where needed.

- For each inspection, the Inspector must determine if the Construction site is in compliance with the CGP, or not.  The Inspector must check the appropriate check-box on Page 1 of the inspection report.

- Each report must be signed and dated by the Inspector, and forwarded to the Construction Manager within 24-hours of the inspection.

SWPPP Inspection Report Instructions for:

Contractor

- The Contractor must review the SWPPP and sign the Certification Statement for Contractor in Section 8.

- The Contractor shall designate a certified SWPPP Inspector, per the latest RIDOT Specifications.

- After an inspection has been performed, the Contractor must sign the ‘acknowledgement’ certification on Page 1 of the Inspection Report at time of receipt from the Construction Manager.

- The RE will provide a copy of the signed Inspection Report to the Contractor.

- The Inspection Report serves as your RIDOT directive to proceed with corrective actions.

- In accordance with the SWPPP and Section 212 of the RIDOT Standard Specifications, the Contractor will commence with the requisite cleaning and maintenance measures
no later than the next consecutive calendar day after receiving such a directive from the Construction Manager, and will aggressively and expeditiously perform such cleaning and maintenance work until the original problem is remedied to the complete satisfaction of the Construction Manager.

- The CONTRACTOR is responsible for maintaining the CORRECTIVE ACTION LOG.

SWPPP Inspector, Construction Manager, & Contractor

Amendments

The SWPPP shall be amended whenever there is a change in design, construction, operation, maintenance or other procedure which has a significant effect on the potential for the discharge of pollutants, or if the SWPPP proves to be ineffective in achieving its objectives.

SWPPP Amendments may be recommended by any party, but all amendments must be approved by the Construction Manager.  The revision must be recorded in the Record of Amendments Log Sheet within the SWPPP, and dated red-line drawings and/or a detailed written description must be appended to the SWPPP.  Inspection Forms must be revised to reflect all amendments by the Inspector.

Questions

Questions may be addressed to the RIDOT Environmental Division, 360 Lincoln Ave., Warwick, RI 02888, 401-734-4892, dot.swppp@dot.ri.gov .

RIDOT Large Site SESC Inspection Report

(February 2022)

| Project Information |
| --- |
| Project Name & RIC#: |  |
| Environmental Permits | Check all applicable to project site: | Permit Number |
|  | ☐Yes | RIPDES CGP (construction) |  |
|  | ☐Yes | RIPDES RGP (contaminated dewatering) |  |
|  | ☐Yes | Freshwater Wetlands/CRMC |  |
|  | ☐Yes | Contaminated Soils? | Soil Management Plan ☐Yes ☐No |
| RIDOT Project Manager | Name | Phone | Email |
| RIDOT Construction Mgr | Name | Phone | Email |
| Operator/Contractor | Name | Phone | Email |
| Contractor SWPPP Contact | Name | Phone | Email |
| Inspection Information |
| Certified SWPPP Inspector | Name & Certification/# | Phone | Email |
| Inspection Date | Click or tap to enter a date. | Start/End Time |  |
| Inspection Type ☐Weekly ☐Pre-storm Event ☐During Storm Event ☐Post-Storm Event ☐Other |
| Weather Information |
| Last Rain Event Date: Click or tap to enter a date. Duration (in hrs): Approximate Rainfall (in): |
| Rain Gauge Location & Source: |
| Weather at time of this inspection: |
| Certification Statements |
| Check statement that applies then sign and date below: ☐ I, as the designated SWPPP Inspector, certify that this site has been inspected as required by regulation and I have determined that maintenance and corrective actions are not required now. ☐ I, as the designated SWPPP Inspector, certify that this site has been inspected as required by regulation and I have made the determination that the site requires corrective actions. The required corrective actions are noted within this inspection report. |
| Inspector | Print Name | Signature | Date |
| The Site Operator & RIDOT Construction Manager acknowledges by his/her signature, the receipt of this SWPPP inspection report and its findings. He/she acknowledges that all recommended corrective actions must be completed and documentation of all such corrective actions must be made in this inspection report per applicable regulations. |
| Operator | Print Name | Signature | Date |
| RIDOT CM | Print Name | Signature | Date |

| Section A: Soil Erosion, Runoff, Sedimentation, & Pollution Prevention Control Measures |
| --- |
| Permit Requirements | If “No”, corrective action is required. Specify action/date & INCLUDE PHOTO #. |
| Minimize Area of Disturbance |
| A1 | Has the operator marked and adhered to the approved LOD on site, including sensitive areas? | ☐Yes ☐No |  |
| Establish Sediment Barriers |
| A2 | Has the operator properly installed and maintained sediment barriers as required along the LOD to retain sediment on site? | ☐Yes ☐No |  |
| Protect Storm Drain Inlets |
| A3 | Has the operator protected all storm drain inlets/grates from construction runoff? | ☐Yes ☐No ☐No inlets in project area |  |
| A4 | Has the operator cleaned and maintained inlet protection measures to maintain performance? | ☐Yes ☐No |  |
| A5 | Has the operator removed accumulated sediment adjacent to inlets within 24 hours of detection? | ☐Yes ☐No |  |
| Establish Temporary Controls for the Protection of Post-construction Stormwater Control Measures |
| A6 | Has the operator protected all areas for proposed infiltration/STUs from compaction, excluded them from work/staging areas, & installed sediment barriers around them? | ☐Yes ☐No ☐No STU proposed |  |
| Preserve Topsoil / Protect Stockpiles |
| A7 | Has the operator covered and/or installed sediment barriers around any stockpiles on site? | ☐Yes ☐No ☐No stockpiles |  |
| Divert or Manage Run-on from Up-gradient Areas |
| A8 | Is the operator preventing water from outside the approved LOD/project area from entering the construction site? | ☐Yes ☐No |  |
| Properly Design Constructed Stormwater Conveyance Channels |
| A9 | Did the operator correctly install and maintain temporary measures, as necessary, to control stormwater traveling through or around the site? | ☐Yes ☐No ☐N/A |  |
| Retain Sediment On-site |
| A10 | Is the operator retaining all sediment on-site? | ☐Yes ☐No |  |
| A11 | Has the operator properly constructed and maintained construction entrances? | ☐Yes ☐No |  |
| A12 | Has the operator properly installed and maintained sediment barriers at the proper interval to protect long, steep slopes from rill and gully erosion? | ☐Yes ☐No ☐No steep slopes |  |
| A13 | Has the operator provided an effective sediment trap for locations that drain more than 1 acre of unstabilized soil? | ☐Yes ☐No ☐N/A |  |
| Stabilize Soils |
| A14 | Has the operator properly stabilized exposed soils where earth disturbance activities have ceased and will not resume within 14 days? | ☐Yes ☐No ☐Working in all areas |  |
| Construction Activity Pollution Prevention Control Measures |
| A15 | If concrete is used on-site, has the operator properly installed, signed, and maintained a washout area within the approved LOD & 50’ from wetlands? | ☐Yes ☐No ☐No concrete |  |
| A16 | Is the operator properly controlling dust? | ☐Yes ☐No |  |
| A17 | Has the operator prevented the release of washout from construction materials? | ☐Yes ☐No |  |
| A18 | Is the operator preventing the discharge of fuels or oils used in vehicle operation through proper storage, availability of spill kits and good operating practices? | ☐Yes ☐No |  |
| A19 | Is the operator properly storing and covering any construction materials & chemicals that have the potential to contaminate stormwater? | ☐Yes ☐No |  |
| A20 | Does the operator have covered designated receptacles for trash and construction debris? | ☐Yes ☐No ☐Removed daily |  |
| A21 | Is the operator removing all construction debris/waste material piles created by the project (i.e. chipped concrete, asphalt, spoils) from the site within 7 days? | ☐Yes ☐No |  |
| A22 | Is the operator street sweeping to prevent accumulated trash and sediment, including track-out, from entering storm drains? | ☐Yes ☐No ☐No storm drains |  |

| Section B: Non-Contaminated Construction Dewatering |
| --- |
| Permit Requirements | If “No”, corrective action is required. Specify action/date & INCLUDE PHOTO #. |
| B1 | If the project has a RIPDES RGP and contaminated dewatering is occurring, is the required treatment system properly installed and maintained per plan? | ☐Yes ☐No ☐No contaminated soils/water |  |
| B2 | If non-contaminated dewatering is occurring on site, is discharge clear and free from turbidity, sediment, foam, or floating solids? | ☐Yes ☐No ☐No dewatering | If no dewatering, Section B of checklist is complete. |
| B3 | Is the operator discharging the treated water to an upland area (not biological wetland) for infiltration? | ☐Yes ☐No |  |
| B3a | If no, is it because it is infeasible to discharge to an upland area? Explain why. | ☐Yes ☐No |  |
| B4 | Has the operator protected all discharge points from erosion? | ☐Yes ☐No |  |
| B5 | Is the operator preventing the captured sediment from being discharged into drains or surface waters? | ☐Yes ☐No |  |
| Section C: Documentation |
| Permit Requirements | If “No”, corrective action is required. Specify action/date. |
| C1 | Are stormwater inspections taking place at least every 7-days & after storm events? | ☐Yes ☐No |  |
| C2 | Have previous Corrective Actions been initiated & completed by the Contractor? | ☐Yes ☐No |  |

Notes:

Site-specific BMPs/Control Measures

Number the structural and non-structural BMPs identified in the SESC Plan on the SESC site plan and list them below. This list may change during construction.	
Note: Corrective Actions are REQUIRED if BMP is not installed or operating properly, or if maintenance is needed to keep BMP from failing.

|  | Location and/or Station | BMP Description | Installed & Operating Properly? | Assoc. Photo # | Corrective Action (CA) | Date Operator Addressed CA |
| --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  | ☐Yes ☐No |  |  |  |
| 2 |  |  | ☐Yes ☐No |  |  |  |
| 3 |  |  | ☐Yes ☐No |  |  |  |
| 4 |  |  | ☐Yes ☐No |  |  |  |
| 5 |  |  | ☐Yes ☐No |  |  |  |
| 6 |  |  | ☐Yes ☐No |  |  |  |
| 7 |  |  | ☐Yes ☐No |  |  |  |
| 8 |  |  | ☐Yes ☐No |  |  |  |
| 9 |  |  | ☐Yes ☐No |  |  |  |
| 10 |  |  | ☐Yes ☐No |  |  |  |

Copy & add more rows if needed.

Photo Log:

(Associated photos – each photo should be dated and have a unique identification # and written description indicating where it is located within the project area.  If a close-up photo is required, it should be preceded with a photo including both the detail area and some type of visible fixed reference point.  Photos should be annotated with Station numbers and other identifying information where needed.)

| Photo #: | Station: |
| --- | --- |
|  | Description: |

| Photo #: | Station: |
| --- | --- |
|  | Description: |

| Photo #: | Station: |
| --- | --- |
|  | Description: |

| Photo #: | Station: |
| --- | --- |
|  | Description: |

| Photo #: | Station: |
| --- | --- |
|  | Description: |

| Photo #: | Station: |
| --- | --- |
|  | Description: |

(copy/paste/add more as necessary)

TO BE FILLED OUT BY RIDOT CONSTRUCTION MANAGER

| OUTSTANDING CORRECTIVE ACTIONS |
| --- |
| Were CORRECTIVE ACTIONS reported in the previous inspection report? |
| ☐ NO | No Corrective Actions were issued in previous inspection report. |
| ☐ YES | ☐ All Corrective Actions have been addressed |
|  | Date work began:Click or tap to enter a date. | Date work completed:Click or tap to enter a date. |
|  | ☐ Corrective Actions remain and are noted in this inspection report. WHY did they not get addressed w/in 7-days? |
| NOTICE TO CONTRACTOR |
| This SWPPP Inspection Report, completed by a Contractor-designated certified SWPPP inspector, indicates that this construction site is: |
| ☐ COMPLIANT | ☐ No immediate actions are required, other than keeping up the good work! (No corrective actions necessary at this time.) ☐ Work is required to maintain site compliance. Corrective Actions are necessary. See below for additional details. |
| ☐ NON-COMPLIANT | This document serves as your RIDOT directive to proceed with CORRECTIVE ACTIONS that have been outlined above. In accordance with the RIPDES CGP, the SWPPP and Section 212 of the RIDOT Standard Specifications, for routine maintenance: the Contractor will initiate work to clean and maintain measures immediately after discovering the problem, and complete the work by close of the next work day after receiving such a directive from the Construction Manager. When installation of a new control or a significant repair is needed, site Contractor must ensure that the new or modified control practice is installed and made operational by no later than seven (7) calendar days from the time of discovery where feasible. |
|  | Date work to begin: Click or tap to enter a date. |
|  | Date work to be completed: Click or tap to enter a date. |
| CM Initials: ____________ CM Comments: Date: |

Corrective Action Log

TO BE FILLED OUT BY SITE OPERATOR
FOR EVERY INSPECTION

|  | Location/Station | Corrective Action | Date Notified | Date Completed | RIDOT Initial |
| --- | --- | --- | --- | --- | --- |
| 1 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 2 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 3 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 4 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 5 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 6 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 7 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 8 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 9 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 10 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 11 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 12 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| 13 |  |  | Click or tap to enter a date. | Click or tap to enter a date. |  |
| Operator Signature: |  | Date: |  |